## Slide 1: RPL

## Slide 2: INDEX
What is RPL
Features
Control messages that RPL uses
How a node choose its parent node
Performing Simulation
Console.log file
Its output, the final list of parent node and sibling node
Attacks and its various effects on RPL

## Slide 3: What is RPL?
RPL stands for Routing Protocol for Low-Power and Lossy networks.
Protocol designed for IoT (Internet of Things) networks with low-power, low-bandwidth, and lossy communication characteristics.
RPL is made to offer dependable and efficient routing in IoT networks with constrained resources. It provides many pathways to the target while minimizing the routing overhead using a directed acyclic graph (DAG) topology.
A set of rules, such as minimum hop count, energy efficiency, and link quality, are used to interconnect nodes to create the DAG.

## Slide 4: Features of RPL
DAG Topology
Energy Efficiency
Adaptive Routing
Scalability
Multicast Support
Security
Traffic Engineering

## Slide 5: Control messages
DIO (DODAG Information Object): DIO messages are sent periodically by the DAG root node to advertise the DAG topology information, such as the DODAGID, the DODAG version number, and the node's rank. The DIO messages are used by the nodes to discover the DAG and join the network.
DIS (DODAG Information Solicitation): DIS messages are sent by a node to request DIO messages from the DAG root node. This message is used when a node joins the network or when a node needs to update its DAG topology information.
DAO (Destination Advertisement Object): DAO messages are sent by a node to inform the DAG root node of its reachability and the routes it can provide. The DAO messages are used to build the routing tables and construct the routes between the nodes.

## Slide 6: Control messages (continued)
DODAG Information Solicitation (DIS) Acknowledgment: DIS-ACK messages are sent by a DAG root node in response to a DIS message. This message acknowledges that the DAG root node has received the DIS message and will send a DIO message in response.
DTSN (DODAG Version Number): DTSN messages are sent by a node to indicate the current version of the DAG. This message is used to ensure consistency across the network and avoid loops in the DAG.
P2P (Point-to-Point): P2P messages are used to establish point-to-point links between the nodes. These messages are used when the node needs to send data to a specific node instead of broadcasting it to the entire network.

## Slide 7: How a node chooses its parent
It selects a parent node based on the following criteria:
Rank : Each node in RPL network has a rank that represents its distance from the root node. Nodes with a lower rank are closer to the root and have a higher priority to become parents.
Link Quality: The link quality between two nodes is measured by the quality of the radio signal between them. Nodes prefer to choose a parent with a better link quality, which means that the data can be transmitted more reliably.

## Slide 8: How a node chooses its parent (continued)
Available Capacity: Nodes also takes account of the available capacity of their potential parent node, which includes the amount of memory, processing power, and battery life.
DODAG Version: RPL allows for multiple DODAGs (Directed Acyclic Graphs) to coexist within the same network. If a node has already joined a DODAG, it is more likely to choose a parent node within that same DODAG to avoid creating a new DODAG.
Based on these criteria, each node in the RPL network selects the parent node with the highest priority to become its preferred parent. The node periodically evaluates the performance of its current parent and may choose to switch to another parent if a better option becomes available.